## Slide 1
Advanced Baseline Imager
Flexible Combined Imager
Advanced Himawari Imager
Ch. No. | Central λ (μm) | λ width (μm) | Resolution (km)
1 | 0.44 | 0.06 | 1.0
2 | 0.51 | 0.04 | 1.0
3 | 0.64 | 0.05 | 1.0 (*0.5)
4 | 0.86 | 0.05 | 1.0
5 | 0.91 | 0.02 | 1.0
6 | 1.38 | 0.03 | 1.0
7 | 1.61 | 0.05 | 1.0
8 | 2.25 | 0.05 | 1.0 (*0.5)
9 | 3.80 | 0.40 | 2.0 (*1.0)
10 | 6.30 | 1.00 | 2.0
11 | 7.35 | 0.50 | 2.0
12 | 8.70 | 0.40 | 2.0
13 | 9.66 | 0.30 | 2.0
14 | 10.50 | 0.70 | 2.0 (*1.0)
15 | 12.30 | 0.50 | 2.0
16 | 13.30 | 0.60 | 2.0
Ch. No. | Central λ (μm) | λ width (μm) | Resolution (km)
1 | 0.47 | 0.05 | 1.0
2 | 0.51 | 0.02 | 1.0
3 | 0.64 | 0.03 | 0.5
4 | 0.86 | 0.02 | 1.0
5 | 1.61 | 0.02 | 2.0
6 | 2.25 | 0.02 | 2.0
7 | 3.88 | 0.22 | 2.0
8 | 6.24 | 0.37 | 2.0
9 | 6.94 | 0.12 | 2.0
10 | 7.34 | 0.17 | 2.0
11 | 8.59 | 0.32 | 2.0
12 | 9.64 | 0.18 | 2.0
13 | 10.40 | 0.30 | 2.0
14 | 11.23 | 0.20 | 2.0
15 | 12.38 | 0.30 | 2.0
16 | 13.28 | 0.20 | 2.0
“Colloquial” channel name | Applications
Blue | aerosol, surface features
Green | aerosol, vegetation
Red | fog, insolation, winds
Veggie | vegetation, winds
Low-Level WV | water vapour, winds
Cirrus | thin cirrus
NIR Phase | cloud phase, snow/ice
Particle Size | particle size, vegetation
Fire | microphysics, fires
Upper-Level WV | WV, winds, rainfall
Mid-Level WV | WV, winds, rainfall
Lower-Level WV | WV, winds, SO2
Cloud-Top Phase | cloud phase, SO2
Ozone | total O3, turbulence
Clean IR | SST, clouds temp
IR Longwave | SST, clouds temp, rainfall
Dirty IR | TPW, dust, ash
CO2 | air temp, cloud height
Proxy instruments - λ(μm) / Res (km) SEVIRI MODIS VIIRS SLSTR |  |  | 
- | 0.44/1.0 | 0.45/0.75 | -
- | 0.55/0.5 | 0.55/0.75 | 0.55/0.5
0.64/3.0 | 0.65/0.25 | 0.64/0.375 | 0.67/0.5
0.81/3.0 | 0.86/0.25 | 0.87/0.375 | 0.86/0.5
- | 0.91/1.0 | - | 
- | 1.38/1.0 | 1.38/0.75 | 1.38/0.5
1.64/3.0 | 1.64/0.5 | 1.61/0.375 | 1.61/0.5
- | - | 2.25/0.75 | 2.25/0.5
3.92/3.0 | 3.75/1.0 | 3.74/0.375 | 3.74/1.0
6.25/3.0 | - | - | -
- | 6.72/1.0 | - | -
7.35/3.0 | 7.33/1.0 | - | -
8.70/3.0 | 8.55/1.0 | 8.55/0.75 | -
9.66/3.0 | 9.73/1.0 | - | -
10.8/3.0 | 11.0/1.0 | 10.8/0.75 | 10.8/1.0
- | - | 11.5/0.375 | -
12.0/3.0 | 12.0/1.0 | 12.0/0.75 | 12.0/1.0
13.4/3.0 | 13.3/1.0 | - | -
Full disc | ✓ | 15 min | 0.5 - 2.0 km
Continental US (CONUS) | 5000 x 3000 km | 5 min | 0.5 - 2.0 km
Mesoscale | 1000 x 1000 km | 0.5 min | 0.5 - 2.0 km
Flex Mode: The flex mode provides a full disk scan every 15 minutes, a CONUS every 5 minutes, and two mesoscale every 60 seconds (or one sub-region every 30 seconds). |  |  | 
MODUS OPERANDI:
Full disc | ✓ | 10 min | 1.0 - 2.0 km
Rapid Scan | LAC 4 (top disc quarter) | 2.5min | 0.5 - 1.0 km
* The channels VIS 0.6, NIR 2.2, IR 3.8 and IR 10.5 are delivered in advanced resolution in the rapid sampling configuration. |  |  | 
Full disc | ✓ | 10 min | 0.5 - 2.0 km
Japan region | 2000 x 1000 km | 2.5 min | 0.5 - 2.0 km
Target area | 1000 x 1000 km | 2.5 min | 0.5 - 2.0 km
Landmark area / x2 | 1000 x 500 km | 0.5 min | 0.5 - 2.0 km
IMAGING
Ch. No. | Central λ (μm) | λ width (μm) | Resolution (km)
1 | 0.47 | 0.04 | 1.0
2 | 0.64 | 0.10 | 0.5
3 | 0.86 | 0.04 | 1.0
4 | 1.38 | 0.02 | 2.0
5 | 1.61 | 0.06 | 1.0
6 | 2.25 | 0.05 | 2.0
7 | 3.90 | 0.20 | 2.0
8 | 6.19 | 0.80 | 2.0
9 | 6.95 | 0.40 | 2.0
10 | 7.34 | 0.20 | 2.0
11 | 8.50 | 0.40 | 2.0
12 | 9.61 | 0.40 | 2.0
13 | 10.35 | 0.50 | 2.0
14 | 11.20 | 0.80 | 2.0
15 | 12.30 | 1.00 | 2.0
16 | 13.30 | 0.60 | 2.0
N E W G E O I M A G I N G M I S S I O N S

## Slide 2
LIGHTNING DETECTION
SOUNDING
Geostationary Lightning Mapper
Lightning Imager
Lightning Mapping Imager
GOES-16
GEO
CCD camera operating at 777.4 nm (O2) to count flashes and measure their intensity
Electronic, 3-axis stabilised satellite, single detector matrix
8 km at s.s.p. (sub-satellite point)
Large fraction of the disk continuously observed (time resolution 2 ms)
MTG-I
GEO
CCD camera operating at 777.4 nm (O2), flash counts and intensity measurement. Detection efficiency > 90 % for events of 10 µJ·m-2·sr-1 at 45° (day), 4 µJ·m-2·sr-1 (night). FAR < 2 s-1
Electronic, 3-axis stabilised satellite, single detector matrix
10 km
Full disk continuously observed (time resolution ~ 2 ms)
Feng-Yun-4
GEO
CCD camera operating at 777.4 nm (O2) to count flashes and measure their intensity
Electronic, 3-axis stabilised satellite, single detector matrix
7.8 km at s.s.p.
Full disk continuously observed (time resolution ~ 2 ms)
TRMM/ISS
LEO
CCD camera operating at 777.4 nm (O2) to count flashes and measure their intensity
Pushbroom, matrix array of 128 x 128 detectors, swath 600 km; each earth location observed continuously (every 2 ms) for about 90 s
4 km
Passes at ~ 100-min intervals with longer gaps once or twice per day. More regular coverage at 15°N and 15°S. On ISS: latitude coverage extended to 51.6°
Pioneer instrument - LIS
~
~
A network of sensors operating in the Very Low Frequency (VLF) band and measuring horizontal magnetic fields of radio impulses generated by return strokes and large cloud pulses.
Fixed location, ground-Based detectors
2-3 km
Global
Ground network - GLD360
Platform
Orbit
Description
Scanning technique
Resolution
Coverage /Cycle
Infra-Red Sounder
Geostationary Interferometric IRS
MTG-S
GEO
Interferometer with large detector arrays for simultaneous sounding of more pixels
Mechanical, bi-axial, 3-axis stabilised satellite, step-and-dwell of a detector matrix
4.0 km
Full disk in 60 min. Limited areas in correspondingly shorter time intervals
Feng-Yun-4
GEO
MWIR/TIR interferometer with large detector arrays for simultaneous sounding of more pixels. 913 channels on the first flight unit, 1188 on follow-on flight units.
Mechanical, bi-axial, 3-axis stabilised satellite, step-and-dwell of a detector matrix.
Prototype flight 16 km, follow-on 8 km, at s.s.p.. Supporting VIS: 2 km at s.s.p.
China area (5000 km x 5000 km) in 67 min. Mesoscale area (1000 km x 1000 km) in 35 min
EPS-A/B/C
LEO
Interferometer with 8461 channels, with one embedded IR imaging channel
Cross-track: 30 steps of 48 km ssp, swath 2130 km - Along-track: one 48-km line every 8 s
4 x 12-km IFOV close to the centre of a 48 x 48 km2 cell (average sampling distance: 24 km)
Near-global coverage twice/day
Proxy instrument - IASI
Platform
Orbit
Description
Scanning technique
Resolution
Coverage /Cycle
NOAA-20
LEO
Interferometer with three IR bands, 1305 channels in initial operation mode. Future operation mode will have 2211 channels with the same full spectral resolution in all three bands.
Cross-track: 32 steps of 48 km s.s.p., swath 2200 km - Along-track: one 48-km line every 8 s
3 x 3 14 km IFOV covering a 48 x 48 km2 cell (average sampling distance: 16 km)
Near-global coverage twice/day
Proxy instrument - CrIS
N E W G E O L I G H T N I N G M I S S I O N S
N E W G E O S O U N D I N G M I S S I O N S