## Slide 1: Displaying Emagrams and Ingesting Eumetview Data in PUMA-2025

## Slide 2
1 - Load any satellite or NWP product
2 - From the main menu click on 4 grid boxes
3 - From the split view select the 2 vertically separated boxes
4 - From the displayed window click to add new product
5 - Under Layouts, select NWP
6 - Under NWP, select the model to use
7 - Under Runs, select the run time
8 - Under Products, select Emagram
9 - Under Emagram click on all under.
10 - Click on Load to display
11 - To link the Map and the emagram
  11 a- Right-click on the map and check the box double click location event
  11 b - Right-click on the emagram and check the box listen double click location
  Double click on any location on the map to display the emagram at that location
Displaying Emagrams
3
4
5
6
7
8
9
10
11 a
11 b
2

## Slide 3
Displaying Emagrams with PUMA-2025 at a single point
1 - Load the emagram
2 - Click on the setting bouton of the product name
3 - From the display window, click on data to expand
4 - Click on Add point to edit the coordinates of the emagram display
5 - Input the coordinate of the new point
6 - If wished, click on the pencil to reference the point (the name of an airport for example)
2
3
4
5
6

## Slide 4: Accessing EUMETVIEW Data on PUMA

## Slide 5
1 Open Queue
2 From the drop-down menu click on EUMETVIEW under Layouts
3 Select the source of the product to display (MTG or MSG)
4 Select product under channels
5 Under images set the display characteristics (period (under From), under range and interval (under every)
6 Click on load to display
Accessing EUMETVIEW Data on PUMA
5