## Slide 1: Kalman Filter simultaneous retrieval of surface emissivity and temperature from SEVIRI data
Applied Spectroscopy
Giuliano Liuzzi, Guido Masiello, Carmine Serio and Sara Venafra.
School of Engineering, University of Basilicata, Potenza
Presented by Carmine Serio

## Slide 2: Brief outline
Background
Aim and scope
Basic methodology
Results with emphasis on potential land cover change detection applications
Conclusions

## Slide 3: Why we developed the KF for SEVIRI
The work originated within EUMETSAT (P. Watts)
  Objective: To study and formulate a general strategy to apply spatial and temporal constraints to the estimation of geophysical parameters from radiance measurements made from geostationary platforms, to apply the strategy to a particular example problem and to recommend a way forward to more general application to MTG FCI imager and IRS sounder data.
The study was also motivated by the quest of methodologies capable to perform a dimensionality reduction of the data space
  In NWP the numbers of observations varies considerably, but global models perhaps assimilate of order 106 observations per 12 hour window. With SEVIRI the number of observations is of order 108 per 15 minutes.

## Slide 4: Background
Continuity is felt important in order to dynamically separate emissivity from temperature. In order words, try to exploit the different variability time scale of the two: minutes for temperature, days for emissivity.
Dimensionality reduction is felt important also in view of MTG: FCI and IRS mission

## Slide 5: Kalman Filter
KF is an assimilation system (may incorporate the basic physics involved in the problem: radiative transfer and dynamics).
Acting on the dynamics, we can put appropriate constraint in order to take advantage of the different time scale of emissivity and temperature.
Exploiting the time sequential architecture of KF, the dimensionality of the data space is kept scalar in time, i.e., observations are processed as they come and are not accumulated as it would be in an ordinary static Optimal Estimation method.

## Slide 6: KF development for SEVIRI, funding
Studies have started since since 2011 and funded by
EUMETSAT
  “Study on space-time constrained Parameter Estimation from Geostationary data”, Contract # EUM/CO/11/4600000996/PDW:
  “Kalman Filter estimation of surface temperature and emissivity from SEVIRI", contract EUM/CO/14/4600001329/PDW
The RITMARE flagship project, National Research Council, CNR

## Slide 7: KF development for SEVIRI, publications

## Slide 8: Acknowledgements
Isabel Trigo, Instituto Portugues do Mar e da Atmosfera IP, Land SAF, Lisbon, Portugal
Frank M. Göttsche, Karlsruhe Institute of Technology (KIT), Karlsruhe, Germany

## Slide 9: Kalman filter
observation equation
state/evolution equation
update or analysis
forecast
forecast
at time t
covariance of ƞt
analysis
at time t
Application to SEVIRI window channels, for the retrieval of Surface Temperature (Ts) and emissivity (ε)
  Masiello, G. et al. 2013, Atmos. Meas. Tech., doi:10.5194/amt-6-3613-2013

## Slide 10: Forward Model
σ-SEVIRI is a monochromatic radiative transfer model:
  It computes Spectral High-resolution quantities
  Then it convolves them with the SEVIRI ISRF
  The code is suitable for general purpose
  It takes into account both Specular and Lambertian reflection
  It is based on look-up table of optical depth + interpolation procedure
  Simple dependence of the Optical Depth with respect to the Temperature and the gas concentration
  Analytical derivative, Fast and Accurate
  Specular and Lambertian models for the reflected radiance term

## Slide 11: Further constraint, maximum-minimum channel emissivity difference
Three bands
Four bands

## Slide 12
SEVIRI spectral response functions over-imposed to a typical IASI spectrum
Ch. 7 @ 12 μm
Ch. 6 @ 10.8 μm
Ch. 4 @ 8.7 μm
Ch. 5 @ 9.7 m

## Slide 13: Background Information, Atmospheric State
ECMWF Operation Analysis from MARS platform.
High spatial Resolution (0.125x0.125)
91 Pressure levels until June 25th 2013
137 Pressure levels from June 26th 2013
SKT, Skin temperature
SP, Surface Pressure
TCC, Total Cloud Cover
T, Temperature
Q, Specific Humidity
O3, Specific Ozone
ECMWF, Surface temperature

## Slide 14: Background Information, Emissivity
UW/BFEMIS, database, Monthly mean and covariance computed for the 10 years period 2003-2012.
ECMWF, Skin temperature

## Slide 15: Results from the three LSA SAF validation stations Comparison with in situ Surface Temperature
 | Mean difference with in situ data (°C) | Standard deviation of the difference (°C)
Dahra Jan.-to Oct. 2011 | -0.70 | 0.96
Evora Jan. to Dec. 2010 | +0.91 | 1.62
Gobabeb Jan. to Dec. 2010 | +0.86 | 1.18

## Slide 16: An example from Dahra station

## Slide 17: Emissivity Retrieval (Evora Station)

## Slide 18: Emissivity Retrieval (Gobabeb Station)

## Slide 19: Comparison with ECMWF data show excellent agreement (statistics based on 2,754,238 data points)

## Slide 20: Comparison with MODIS shows a bias of 0.07 K and a standard deviation of 1.05 K (statistics based on 3,230,710 data points)

## Slide 21: Applications to Full Disk and Regional scale
MSG-9 and MSG-10 SEVIRI Pixels with VZA <= 70°
Full Disk Definition an Applications

## Slide 22: November 2007 surface temperature

## Slide 23: November 2007, Emissivity at 8.7 m

## Slide 24: November 2007, Emissivity at 10.8 m

## Slide 25: November 2007, Emissivity at 12.0 m

## Slide 26: November 2007, Checking differences vs UW/BFEMIS

## Slide 27: Applications to the regional scale Case Studies: Basilicata
SEVIRI observations recorded during the whole year 2013
MSG-10 SEVIRI Pixels with
13 ≤ Lon ≤ 18.875
39.25 ≤ Lat ≤ 42
9643 Pixels
4374 Over Land
5269 Over Sea

## Slide 28: Retrieved Skin Temperature, whole year 2013
http://www2.unibas.it/gmasiello/assite/Basilicata_2013_TsLand.gif
http://www2.unibas.it/gmasiello/assite/Basilicata_2013_TsSea.gif

## Slide 29: Retrieved Skin Temperature, 1 Day of August
http://www2.unibas.it/gmasiello/assite/basilicata_Aug_2013.gif

## Slide 30: Land cover change detection with infrared SEVIRI channels

## Slide 31: Land cover change detection, an example from Evora, Portugal

## Slide 32: Land cover change detection, an example from Dahra, Senegal

## Slide 33: Application to the regional scale: Negev (Israel)
SEVIRI observations recorded from May to September 2013
Notes: Because of grazing and wood gathering activities the dunes in the Negev have been covered by biocrusts and consequently have been stabilized

## Slide 34: Work in collaboration
Diurnal Emissivity Dynamics in Active Sand Dunes vs. Dunes Stabilized by Biocrust
Offer Rozenstein1, Nurit Agam1, Carmine Serio2, Guido Masiello2, Sara Venafra2, Stephen Achal3, Eldon Puckrin4, and Arnon Karnieli1
Jacob Blaustein Institutes for Desert Research, Ben-Gurion University of the Negev, Sede Boker Campus 84990, Israel.
School of Engineering and CNISM, Potenza Research Unit, University of Basilicata, Potenza, Italy.
ITRES Research Ltd. #110, 3553 31st Street N.W. Calgary, Alberta, T2L 2K7, Canada.
Defence Research and Development Canada (DRDC) - Valcartier, 2459 de la Bravoure, Québec, QC, G3J 1X5, Canada.

## Slide 35: Anthropogenic activity on the Israel side has changed surface emissivity

## Slide 36: The emissivity change is very well captured by SEVIRI channel emissivity at 8.7 m
Map of the area
SEVIRI channel emissivity at 8.7 m

## Slide 37: Negev (Israel) case study
Emissivity @ 8.7 µm for August 2013

## Slide 38: The code has been developed in Fortran language and installed at EUMETSAT

## Slide 39: The code can run from the level of the single pixel up to the SEVIRI full disk scale
Single Pixel
Full disk

## Slide 40: Full Disk (data input for one day cycle)
ECMWF
  |Latitude|<=82°; |Longitude|<=82°;
  step 0.125°
  Nlat=1313; Nlon=1313
  Nlev=91 or 137
  Parameters:
    T,W,O (Nlev), SKT
  Nlat*Nlon*(3*Nlev+1)
    (4.7x108 or 7.1x108)×5
SEVIRI
  (Nrow=3395)×(Ncol=3389) ×96 ×8;

## Slide 41: Regional Area (one day cycle)
ECMWF
  39.5°<=Latitude<=42°; 13<=Longitude<=18.75°;
  Step 0.125°;
  Nlat=23; Nlon=47
  Nlev=91 or 137
  Parameter:
    T,W,O (Nlev), SKT
  Nlat*Nlon*(3*Nlev+1)
    (3.0x105 or 4.5x105)×5
SEVIRI
  (Nrow=166)×(Ncol=71) ×96 ×8;

## Slide 42: Single Pixel (one day cycle)
ECMWF
  Latitude=round(Latsev*8)/8
  Longitude=round(Lonsev*8)/8
  Nlat=1; Nlon=1
  Nlev=91 or 137
  Parameter: T,W,O (Nlev), SKT
  3*Nlev+1
    (274 or 412)×5
SEVIRI
  (Nrow=1) ×(Ncol=1)×96×8;

## Slide 43: Performance
CPU Intel Xeon E5 2697 12 Core 2.7 GHz 30MB 150W
128 GB of RAM
It takes about 1÷1.3 minutes to retrieve (Ts,) for one pixel for a whole month

## Slide 44: Conclusions and remarks
The KF retrieval system can be used at the regional or global scale.
On regional scale the system can be run in real time and, therefore, used together with statistical image tools for natural and anthropic hazard alarms. Off-line, it could be used for risk assessment analysis and for land cover change detection.
KF has the unique feature to simultaneously retrieve surface emissivity and temperature
SEVIRI emissivity maps do not exist yet. KF could provide full disk monthly emissivity maps
The emissivity maps could be used as additional input for land use / land cover change analyses and would be beneficial for many Ts statistical retrieval algorithms for SEVIRI, which largely rely on the availability of the channel emissivity at 10.8 m and 12 m.
This availability would improve the exploitation of the European geostationary platforms and also lead to a better exploitation and improved usage of other European satellite systems.

## Slide 45: CINFAI-CNISM-UNIBAS-IMAA/CNR applied spectroscopy group http://www2.unibas.it/gmasiello/assite/as/home.html