## Slide 1
5th SALGEE Workshop
18-20.09.2017
Yerevan, ARMENIA
Software Development for Decoding of NOAA VIIRS Active Fire EDRs
Erdem ERDİ
Turkish State Meteorological Service

## Slide 2
Outline
Initial HDF-EOS fire product
Switch from HDF-EOS to NetCDF
Decoding software and possible options
Validation plan for NPP fire products over Turkey
1

## Slide 3
Initial HDF-EOS fire product
M-Bands (750 meter spatial resolution) on VIIRS instrument
HDF-EOS (HDF-4 based)
Swath based, 6 minutes PGE (Product Generation Executable)
Obtained from NASA/NOAA archive
2

## Slide 4
Switch from HDF-EOS to NetCDF
E-mail from EUMETSAT Operations Center:
In February 2017, the distribution on EUMETCast of the MODIS Fire Product had to be suspended due to a significant increase in the file size following the transition at NASA from MODIS Collection 5 product processing to Collection 6 product processing.
We have no plan to resume the distribution of the MODIS Fire Product but we will replace it with the VIIRS Active Fire (AF) Product from NOAA. The VIIRS fire detection algorithm is an adaptation of the MODIS Collection 6 algorithm and uses Level 1 M-band data from the VIIRS instrument.
3

## Slide 5
Switch from HDF-EOS to NetCDF
A trial dissemination of the VIIRS AF product will start on 30 August 2017.
The product will be distributed on EUMETSAT Data Channel 12:
PID: 301 (Europe and Africa)
Multicast address: 224.223.222.35
Example filename:
AF_v1r0_npp_s201706281434280_e201706281435520_c201706281619150-122800_0.nc.gz
There will be 500 files /12h i.e. 1000 files /day, with a size of around 111 MB per day.
4

## Slide 6
Decoding software and possible options
Being developed in C++ (although the Python was another possibility)
Command-line operation
Suitable for both the operational use and off-line use
Cross-platform (Windows & Linux)
- Which Linux distro ?
- Area of Interest (AOI) to be definable
Major user needs regarding the product decoding
(next slides)
5

## Slide 7
Decoding software and possible options
Text Output
- Formatted style (better for visual inspection)
- Comma Seperated Values (CSV) is good in case the file is to be used in javascript code (?)
Common Alerting Protocol (CAP) (?)
    XML-based data format for exchanging public warnings and emergencies between alerting technologies.
6

## Slide 8
Decoding software and possible options
Graphics Based Outputs
- Fire locations plotted on geographical maps
Google Maps Outputs (?)
    KML files for using on Google Earth & Google Maps
ShapeFile Outputs (?)
    De-facto standard for GIS applications
    Related .dbf files should also be created with corresponding fire event information
7

## Slide 9
Validation plan for NPP fire products over Turkey
EUMETSAT FIR product validation studies were performed in the past.
Validation of the products against fire records of Ministry of Forestry is planned for the years of 2015-2017.
Sharing of the NRT fire detections of VIIRS products depending on the results.
8

## Slide 10
Validation plan for NPP fire products over Turkey
Thank you for your attention.
eerdi@mgm.gov.tr
8