## Slide 1: New LSASAF Fire Emission product
Presenter: Tianran Zhang
Contribution from: Martin Wooster, Hannah Nguyen, Jiangping He, Weidong Xu, Tianran Zhang
Notes: Exploti geo data since GFAS hasn’t done that

## Slide 2: Background: Biomass Burning Atm. CO2 Contribution
Fire CO2 emissions average 2.0 Pg C yr-1
Deforestation & forest degradation is 2nd largest anthropogenic CO2 source after fossil fuel combustion.
Together estimated as ~ 15% of net global annual average CO2 emissions.
With a mean emission rate of 11.3 Tg CO2 per day during Sept-Oct 2015, emissions from these fires exceeded the fossil fuel CO2 release rate of the European Union (EU28) (8.9 Tg CO2 per day).

## Slide 3: Background: Biomass Burning Emissions
Biomass burning a major air pollution source (PM2.5, VOCs, tropospheric O3, CO..).
Respiratory effects.
SE Asia + 200 days/yr-1 > WHO AQ targets.
Indonesia peat burning in 09/2019
Notes: Main issue: aerosol emission

## Slide 4: Biomass Burning Emissions Calculation
Ei = BA x FL x CC x EFi
Ei = FRE x CF x EFi
burnt biomass
sat. obs.
(dynamic) veg. model
land cover map
believed
~ constant
“key uncertainties” (Reid et al. 2009)
Ei = emission of species i [kg)]
Ei = emission of species i [kg(species i)] BA = burnt area [m2]
CC = combustion completeness [kg(burnt fuel) / kg (available fuel)]
EFi = emission factor for species i [kg(species i) / kg(biomass)] FL = fuel load [kg(biomass) / m2]
FRP = fire radiative power [MW] FRE = Fire Radiative Energy [MJ] = ∫ FRP(t) dt
CF = combustion factor [kg(biomass) / MJ (FRE)]
Global Fire Emissions
Database (GFED)
Daily FRP
(single fire)
Geostationary FRE
(Roberts and Wooster, 2008)
Notes: Gfed is not good for real time
Concersion factor is consistant (CF) no matter what you burn

## Slide 5: Fire Radiative Energy & Fuel Consumption
Slope is the “combustion factor” CF linking FRP directly to fuel consumption.
Fuel Consumption =  FRP  CF
CF = 0.37 kg.MJ-1

## Slide 6: GFAS MODIS-estimated FRE to GFED3.1 Fuel Consumption
Derivation of conversion factors (CF) from linearly regressing monthly GFED3.1 DM with GFAS1.0 FRE
Cfsmall scale = 0.37 g kJ-1
Savanna
Forest
Kaiser et al. (2012) Biogeosciences
SA: Savanna AG: Agricultural
DF: Tropical PE: Peat
EF: Extratropical
“OM” = with organic matter burning
Notes: Small fires missed
Tree block
FRE from modis denial cycle might be not captured very well
GFAS get round by comparing FRE to GFED
This method is good but can only as good GFED ever

## Slide 7
Aqua-MODIS
15 Sept 2014
Sept 2014
Jan 2015
April 2014
Copernicus Atmosphere
Monitoring Service (CAMS)
Global Fire Assimilation System (GFAS)
MODIS FRP Based

## Slide 8: Biomass Burning Carbon Emission from CAMS-GFAS

## Slide 9
Meteosat SEVIRI and African Fire Radiative Power Retrievals
Wooster et al. (2015) ACP, 15, 13217-13239
Delivered by EUMETSAT LSA SAF every 15 mins - https://landsaf.ipma.pt/
LSA SAF Meteosat FRP-PIXEL Product
Notes: Ideal by bapass the method of GFAS

## Slide 10: Smoke Plume Delineation
SEVIRI Active Fire Detections
MODIS AF Detections
MODIS AF Detections Remapped
MODIS 10 km AOD Product

## Slide 11: Developing and Evaluating a top-down approach for Emission Estimates
Methodology
1) Generate a dataset of match-ups between FRP and Total Particulate Matter derived from AOD measurements
2015
Notes: Aod correlation with total particular matter
Controlled by a conversion value

## Slide 12
2) Combine EO Landcover and Tree cover maps
Tree Cover Landsat-8 (30 m)
CCI Landcover (MERIS 300 m)
3) Classify plume-FRP match-ups by biome and use the relation between total TPM and FRP to derive biome specific emission coefficients
4) Use the derived Emission inventory in a CTM to evaluate the results against satellite and ground observations of AOD
Notes: 5/6 classes
Cooffiecnt can just apply forward, not change in between years, only for landcover

## Slide 13: TPM Emission Product Density
TPM Emissions Density [g.m-2]
Notes: GFAS a factor of 3 to match
So this is like to be correct

## Slide 14: TPM Emission Rate - Southern Africa August 2012 Temporal Detail
Emission of species X = TPM Emissions . EFx / EFTPM
Notes: Temporal detail, huge daily variety
Better for input in transport model
Convert total particulate to other emissions
CO, CO2, CH4, and total carbon 15min 1day
Next half year, demo mode.