## Slide 1: Major advances of LSA SAF FRP-PIXEL Product
Martin J. Wooster, Weidong Xu,
Gareth Roberts,
And Jiangping He
Background
FRP-PIXEL
Applications
SALGEE 2019 workshop Darmstadt
14-17 Oct 2019
SEVIRI

## Slide 2: Radiative Transfer of Active Fire Detection

## Slide 3
Planck Function
MIR approach
FRP (MW) corresponds to the ‘radiative strength’ of fire in a pixel, correlating to its rate of fuel combustion and smoke release.
Fire Radiative Power Derivation

## Slide 4: Operational SEVIRI FRP-PIXEL List Product
Delivered operationally to all as part of EUMETSAT Land Surface Analysis Satellite Applications Facility (LSA SAF)
Landsaf.meteo.pt/
>99% process success
15 mins temporal resolution
Product available in 2 hours after overpass
Input to CAMS

## Slide 5: Operational SEVIRI FRP-PIXEL Quality Product
Delivered operationally to all as part of EUMETSAT Land Surface Analysis Satellite Applications Facility (LSA SAF)
Landsaf.meteo.pt/
>99% successful process rate
15 mins temporal resolution
Product available in 2 hours after overpass

## Slide 6: Example Wildfire - July ‘09 Spain
Fire expanded & burned initially exactly matching News reports.
Fire flared again on 23rd July, as illustrated in FRP-PIXEL product.

## Slide 7: SEVIRI - Fire Diurnal Cycle
Fire Diurnal Cycles
FROM MODIS

## Slide 8: Summery
FRP-PIXEL: A LSA SAF operational product for ~10 years now;
FRP-PIXEL provides the only genuine full fire diurnal cycle information over Africa and Europe;
The product is the only geostationary fire product operationally currently injected into the CAMS global fire assimilation system.

## Slide 9: Global Fires from MODIS
1 km resolution – very sensitive to fires - but ONLY 4 passes per day.
Global database – useful for evaluation of other products.

## Slide 10: Diurnal cycles
Active Fire Pixel Comparison: FRP-PIXEL & MODIS
Error of omission: 67%
Error of commission: 8%

## Slide 11: WFABBA filtered (201408)
False alarm from WFABBA show a random spatial pattern. No abrupt hot area in the map.
FRP-Pixel: Comparison to Alternative SEVIRI Active Fire Products – 21 Aug 2014
Active Fire Pixel Counts
FRP-PIXEL : 1249
WFABBA : 686
FDeM : 346
FIR : 312
FRP-Pixel
WFABBA
FDeM
FIR
All @ 13:15 UTC

## Slide 12: Active Fire Detection Performance : SEVIRI Fire Products vs. MODIS
Chart: SEVIRI Fire Pixel Count
| FRP-PIXEL | ABBA | FDeM | FIR
Total detection | 26113 | 18547 | 8262 | 5661
Omission error (percent) | 77 | 84 | 92 | 95
1 Month Active Fire Error of Omission

## Slide 13: Active Fire Detection Performance : SEVIRI Fire Products vs. MODIS
Chart: SEVIRI fire pixels
| FRP-PIXEL | WFABBA | FDeM | FIR
Total detection | 33414 | 13008 | 7664 | 7151
Confirmed by MODIS | 29037 | 12284 | 7260 | 6730
Commission error (percent) | 13 | 6 | 5 | 6
1 Month Active Fire Error of Commission

## Slide 14: Summery
FRP estimates agree well between MODIS and SEVIRI on ‘per fire’ basis;
FRP-PIXEL product is based on very sensitive Fire Thermal Anomaly (FTA) active fire detection algorithm, which detects far more active fire pixels than other products based on SEVIRI with similar false alarm rate;
FRP-PIXEL is the only product that provides an FRP value in addition to an active fire detection.

## Slide 15
Copernicus Atmosphere Monitoring Service
SALGEE Project
Advanced Fire Information System (afis.meraka.org.za)
Operational Applications & Science Initiatives

## Slide 16
12 years Climatological reprocessed FRP-Pixel data (2004-2015)

## Slide 17
New Operational FRP products over India Ocean
FRP-Pixel over Europe & Africa FRP-Pixel over India Ocean

## Slide 18: FRP from Himawari-8
Xu, W., Wooster, M. J., Kaneko, T., He, J., Zhang, T., & Fisher, D. (2017). Major advances in geostationary fire radiative power (FRP) retrieval over Asia and Australia stemming from use of Himarawi-8 AHI. REMOTE SENSING OF ENVIRONMENT, 193, 138-149.

## Slide 19: GOES-R & SLSTR FRP
Sentinel-3

## Slide 20: Global Geostationary FRP Observation System
GOES-E
GOES-W
MSG
Himawari-8
0
-40
-80
-120
-160
40
80
120
160
80
60
40
20
0
-20
-40
-60
-80
Satellite
View Angle
80°
65°
MSG-India
Satellite | Bands | SSR (KM) | Full Disk Coverage | MWIR Saturation Temperature (K)
GOES-16 ABI | 2 visible 4 near-IR 10 IR | 0.5 1.0 2.0 | 15 mins | 400
MSG SEVIRI | 3 visible 1 near-IR 7 IR | 1.0 3.0 3.0 | 15 mins | 335
Himawari-8 AHI | 3 visible 3 near-IR 10 IR | 0.5 1.0 2.0 | 10 mins | 400

## Slide 21
Future Missions - Plan for CDOP-3
MTG FRP-PIXEL (Day 1: 2km product, followed by 1 km product testing for possible implementation).
MTG FRP-PIXEL European Rapid Scan (Day 2)
MTG FRP-GRID (Day 2)
MTG Fire <Carbon> Emissions (Day 2)

## Slide 22: Applications
Fuel consumption;
Aerosol optical depth;
Smoke emissions;
Air quality monitoring.