## Slide 1: Agenda - Day 2 12 May, 10:00 CET: Copernicus Atmosphere Monitoring Service products for monitoring fire emissions and smoke (Mark Parrington, Copernicus Atmosphere Monitoring Service - CAMS, European Centre for Medium-Range Weather Forecasts - ECMWF).
Please mute your microphone.
Be mindful of background noise.
Better have your video off to avoid connection issues.
Raise your hand in case you need to ask a question or make a comment. You can also drop a message in the chat if you are experiencing technical problems or if you need to communicate with the host and the other attendees.
Enjoy the webinar!
Welcome to the User Workshop and Training on Fire Monitoring – Data Discovery Week webinars
Join the Q&A session from 15:00 to 16:00 CET at slido.com #fireworkshop.

## Slide 2
Mark Parrington (mark.parrington@ecmwf.int)
Discover the Data, Day 2:
Copernicus Atmosphere Monitoring Service products for monitoring fire emissions and smoke
User Workshop and Training on Fire Monitoring, 12 May 2020
Acknowledgements: Sebastien Garrigues, Miha Razinger, Vincent-Henri Peuch, Melanie Ades, Anna Agusti-Panareda, Jerome Barre, Richard Engelen, Johannes Flemming, Antje Innes, Zak Kipling, Martin Suttie, Juan Dominguez, Roberto Ribas, Luke Jones & CAMS development teams
@m_parrington
Notes: while ECMWF has a lot of expertise in the field of data assimilation and NWP, we are fairly new to atmospheric composition modelling
give credit to ECMWF core staff and CAMS partners, focus on collaborations

## Slide 3: Topics addressed in this presentation
The Copernicus programme and services.
The role of observations in the Copernicus Atmosphere Monitoring Service (CAMS).
CAMS products for monitoring global fire emissions and atmospheric impacts.
Other products, and tools, in the CAMS portfolio for understanding air pollution.
Data access.

## Slide 4: WHAT IS COPERNICUS?
Copernicus is a flagship Space programme of the European Union
  to monitor the Earth, its environment and ecosystems
  to ensure its citizens are prepared and protected for security risks and natural or man-made environmental risks and disasters
Copernicus as user-driven Programme
It has full, free and open to all data policy
Is a tool for economic development and a driver for the digital economy
Initiated in 1998, Copernicus became operational in 2014. Budget for 2014-2020 was 4.3 B€. Foreseen budget for 2021-2027 is 5.8 B€.
Notes: obligatory mention of the ambitious and expensive Copernicus programme
something about motivation for services and improving the data access for wider audience
feel that I need to justify

## Slide 5: Why are Copernicus services needed?
Example: NO2 tropospheric column from Copernicus Sentinel-5P (31/10/2018)
Observations are essential, but direct use is generally limited:
gaps in space and time
observed quantities may not be directly relevant (vertical column vs surface concentration)
can be complex and numerous
What services do:
blend observations (satellite and non satellite) with model to provide a consistent 3D state
forecasts, a few days ahead
reanalyses over past years or decades
Notes: it’s the users like you who are really able to answer these vital questions, but based on our user uptake and feedback we feel that our existence is fully justified

## Slide 6: COPERNICUS AND ECMWF
Sentinels
Copernicus is the European Union’s operational Earth Observation and Monitoring programme, looking at our planet and its environment for the ultimate benefit of all citizens.
User-driven with free and unrestricted data access
Atmosphere
Climate
Land
Marine
Emergency
Security
Observations feeding into value-added Services
Service is implemented by ECMWF
ECWMF is contributing to the Service

## Slide 7: Reasons to care about atmospheric composition
from D. Jacob
…but also benefiting NWP
direct effect of aerosols, ozone and greenhouse gases on radiation
effect on cloud formation and precipitation
use in observation operators for satellite radiance assimilation
Notes: Atmospheric composition matters from local to global scales.
some of the ECMWF motivations: effect on radiation budget, interaction between aerosols and cloud formation, cleaning-up/interpreting information from satellite instruments

## Slide 8: Atmospheric science in the ECMWF Integrated Forecast System (IFS)
IFS
Observation operators
Chemical module
CHTESSEL
Bin scheme
TM5-CB05
Aerosol module
Meteorology
4D-Var
GHG module
The CAMS global production system is the ECMWF Integrated Forecast System (IFS).
IFS is the full NWP forecasting and data assimilation system of ECMWF

## Slide 9: CAMS SERVICE CHAIN
CAMS SERVICE CHAIN
Space Agencies
In-situ observations
Users
15
ECMWF Integrated Forecasting System (IFS)
Regional multi-model ensemble (lead: Météo-France)

## Slide 10: Near-real-time satellite data usage
Species | Instruments
Global system | 
O3 | OMI, SBUV-2, GOME-2, MLS, TROPOMI, OMPS, IASI
CO | IASI, MOPITT, TROPOMI
NO2 | OMI, GOME-2, TROPOMI
SO2 | OMI, GOME-2, TROPOMI, IASI
Aerosol | MODIS, PMAp, VIIRS, SLSTR, SEVIRI
CO2 | GOSAT, OCO-2
CH4 | GOSAT, IASI, TROPOMI
GFAS fire emissions | MODIS, GOES-E/W*, SEVIRI*, SLSTR, VIIRS, HIMAWARI-8*
A wide-range of atmospheric composition satellite observations are assimilated in the IFS to produce daily analyses.
Control runs (with no data assimilated) and forecasts (initialised from analyses) are also produced in CAMS.
CAMS data used for field campaign planning and evaluating special events.
Composition data additional to thousands of assimilated meteorological data.
Assimilated Monitored Future
*Geostationary platform

## Slide 11: Assimilated reactive gases in CAMS real-time system
OMI
AURA
SO2
GOME-2 Metop-B
GOME-2 Metop-A
OMI
AURA
GOME-2 Metop-A
GOME-2 Metop-B
Tropospheric NO2
IASI Metop-A
IASI Metop-B
MOPITT TERRA
CO
O3
GOME-2 Metop-A
OMI, MLS
AURA
SBUV/2
NOAA-19
monitored
assimilated
GOME-2 Metop-B
OMPS
SNPP
HCHO
GOME-2 Metop-A
TROPOMI
S5P
TROPOMI
S5P
Notes: better coverage, reducing errors, redundancy, satellite monitoring

## Slide 12: CAMS products families
Solar radiation and UV index
Ozone layer
Bottom-up emissions and surface fluxes of greenhouse gases
Global analyses, forecasts and reanalyses (2003-...)
NO2
European Air Quality and products in support of policy users
Climate forcing estimates
atmosphere.copernicus.eu
Global emissions based on satellite observations
https://atmosphere.copernicus.eu/

## Slide 13: CAMS Service Product Portfolio
Portfolio | Product groups
A. Regional products | Real-time analyses
 | Real-time forecasts
 | Interim annual reanalyses
 | Annual reanalyses
B. Global products | Real-time analyses
 | Real-time forecasts
 | Reanalyses
C. Supplementary products | Policy support products
 | Solar radiation
 | Greenhouse gas flux inversions
 | Climate forcings
D. Emissions products | Anthropogenic emissions
 | Fire emissions
 | Natural emissions

## Slide 14: ESTIMATING GLOBAL WILDFIRE EMISSIONS IN CAMS
Global Fire Assimilation System (GFAS); see http://apps.ecmwf.int/datasets/data/cams-gfas/
Uses satellite observations of Fire Radiative Power (FRP)
  Currently Aqua and Terra MODIS FRP observations
  FRP from VIIRS, Sentinel-3 and geostationary satellites will be added in 2020
Daily global coverage at ~10km resolution
  1-day behind NRT (pre-operational diurnal cycle/hourly output since 2018)
Emissions of aerosols and gases are estimated using factors dependent on vegetation type.
Injection heights calculated with Plume Rise Model and IS4FIRES.
c/o I. Hüser,
J. Kaiser (MPIC) et al.
Upcoming hourly GFAS

## Slide 15: GFAS hourly fire emissions
17 June
20 June
19 June
18 June
Portugal fires 17-22 June 2017: diurnal cycle (including LEO+GEO obs) improves temporal profile of fire emissions

## Slide 16: Long-range transport of boreal fire emissions, August 2017
Fires in Siberia
Fires in Canada
CAMS daily fire CO2 emissions (GFASv1.2)
Mean daily emission 2003-2016
Daily emission 2017
Mean daily emission 2003-2016
Daily emission 2017

## Slide 17: Long-range transport of boreal fire emissions, August 2017
Smoke from fires in NWT crossed the Arctic Circle in mid-August.
Generally good comparison of CAMS AOD with Aeronet observations.

## Slide 18: Long-range transport of boreal fire emissions, August 2018
Thick smoke blanketed much of North America for several weeks leading to significant deterioration in air quality.
Several events of smoke transport across North Atlantic to Europe monitored by CAMS and observed at AERONET sites.
Grand Forks, ND, USA
Halifax, NS, Canada
Graciosa, Azores
Birkenes, Norway

## Slide 19: Monitoring Arctic wildfires during summer 2019
Daily total wildfire emissions were well above the 2003-2018 average throughout the summer north of the Arctic Circle
Many wildfires concentrated in the Sakha Republic, Russia with other fire activity in Alaska, Yukon Territory and Greenland
Total estimated equivalent CO2 of ~170 megatonnes

## Slide 20: Links between CAMS and CEMS: from fire forecasts to emissions
CEMS Daily Fire Danger Forecasts for Central Sweden
Forecast date
10-Jul
09-Aug
CAMS GFAS daily CO2 emissions from wildfires ibn Sweden.
10-day forecasts of fire danger, calibrated for central Sweden between 10 July and 9 August 2018.
Fire danger classes calculated with the Global ECMWF Fire Forecast (GEFF) System.
Daily forecasts available via CEMS EFFIS (for Europe) and GWIS (globally).
Discover the Data - Day 3: ECMWF and Copernicus data offering for assessing and forecasting forest fire danger
c/o C. Vitolo, F. di Giuseppe (ECMWF)

## Slide 21: Monitoring Amazon fires in August 2019
Above average daily fire activity during first 2 weeks of August across the main states of the Brazilian Amazon (also in Bolivia and Paraguay) with smoke predicted by CAMS across much of southern Brazil
Below average (2003-2018) daily activity through September and October shows annual total is not particularly high compared to previous years in GFAS dataset.

## Slide 22: Global analyses and forecasts
40 km horizontal resolution at 137 model levels, pressure levels and single levels
  two 5-day forecasts at 00z and 12z UTC each day
  aerosols (AOD and concentration): biomass burning, dust, sea salt, sulphate
  reactive gases: CO, HCHO, NO2, O3, SO2 + 40 other species
9 km horizontal resolution at 137 model levels; one 5-day forecast per day (CO2, CH4, linear CO)
CO2
CO
AOD
CH4

## Slide 23: Visualizing CAMS forecasts on Windy.com
NO2
PM2.5
AOD
Latest CAMS 5-day global forecasts visualized via website and mobile app of windy.com

## Slide 24: CAMS aerosol case study, Storm Ophelia, October 2017
CAMS aerosol forecasts initialized on 13 October 2017. Storm Ophelia transported a mixture of smoke, dust and sea salt aerosol across Europe leading to the sun appearing red and to yellow skies.

## Slide 25: CAMS global reanalysis 2003 – 2018 (updated yearly)
Global scale
CAMS global reanalysis
2003 – 2018, with new years being added
Aerosols, 13 chemical pollutants, CO2 & CH4
80 km spatial resolution
Inness et al. 2019, https://doi.org/10.5194/acp-19-3515-2019
O3 score at Neumayer station
good
bad
Reanalysis
Real-time

## Slide 26: Assimilated satellite products in CAMS Reanalysis

## Slide 27: CAMS European air quality multi-model ensemble
Individual operational AQ models
Based on a multi-model approach (same boundary conditions, same emissions, same meteo, assimilation of 1000+ surface observations for key species)
DEHM (AARHUS University)
GEM-AQ (IEP)
MINNI (ENEA)
MONARCH (BSC)
Operational AQ ensemble
(incl. spread/uncertainty)
Once daily D+4 forecasts
Regulatory pollutants and pollens
Annual reanalyses
~ 10km resolution
http://www.regional.atmosphere.copernicus.eu
Notes: 27

## Slide 28: High quality products at European scale
Ozone
NO2

## Slide 29: Access the regional air quality forecast data
Data available in GRIB and NetCDF format
You can download it using the CAMS regional data API service:
  https://confluence.ecmwf.int/pages/viewpage.action?pageId=74753748
  http://www.regional.atmosphere.copernicus.eu/index.php?category=data_access&subensemble=api_catalogue

## Slide 30: Regional air quality reanalysis (2010) 2014 - 2018
Data available in NetCDF format
Interim and validated dataset versions
You can download it using the CAMS interactive web interface:
  http://www.regional.atmosphere.copernicus.eu/index.php?category=data_access&subensemble=reanalysis_products

## Slide 31: Products in support of policy users
http://policy.atmosphere.copernicus.eu/DailySourceAllocation.html
Experimental: local vs imported, geographical origin, chemical speciation
Notes: A national environmental institute wants to know what caused the greatly increased pm10 concetrations. Was it local, so that measures could have been taken or was the contamination this time coming from neighboring countries? The CAMS policy instruments provide an initial indication with the sorce receptor tools.

## Slide 32: Products in support of policy users
http://policy.atmosphere.copernicus.eu/CAMS_ACT.html
CAMS_ACT : O3, PM10 (PM2.5 coming)
Assess the effect of emission reductions on daily forecasts
Notes: CAMS also provides emission scenario calculations: what is the effect of a reduction in emissions?

## Slide 33: Access the global analyses and forecasts dataset
Interactive data server:
  https://apps.ecmwf.int/datasets/data/cams-nrealtime
ECMWF Python Web API access
  https://confluence.ecmwf.int/display/WEBAPI
  https://confluence.ecmwf.int/display/WEBAPI/Python+CAMS+real-time+examples
FTP access to real-time data:
  https://confluence.ecmwf.int/display/CKB/FTP+access+to+CAMS+global+data
Latest analyses and forecasts maps:
  https://atmosphere.copernicus.eu/charts/cams/
WMS catalogue:
  https://confluence.ecmwf.int/pages/viewpage.action?pageId=69180318
  https://confluence.ecmwf.int/display/COPSRV/CAMS+WMS+gallery
Requirements:
ECMWF web account
self-registrations
CAMS licence accepted
Requirements:
ECMWF FTP account
registration on request
CAMS licence accepted
Public services

## Slide 34: Accessing CAMS data: Online catalogue
https://atmosphere.copernicus.eu/data

## Slide 35: Accessing CAMS data: Online catalogue
http://atmosphere.copernicus.eu/catalogue
Search criteria based on:
Product family – analysis, forecast (global/regional, emissions/fluxes.
Parameter family – aerosol, greenhouse gas, reactive gas, radiation
Parameter – e.g. organic matter aerosol concentration/AOD for smoke
Products found

## Slide 36: Accessing CAMS data
https://apps.ecmwf.int/datasets/data/cams-nrealtime/
Surface or 3-D fields
Time period
Analysis time
Forecast time
Parameter

## Slide 37: Accessing CAMS data
https://apps.ecmwf.int/datasets/data/cams-nrealtime/
Time period
Parameter
Download

## Slide 38: Atmosphere Data Store (ADS)
https://ads.atmosphere.copernicus.eu/cdsapp#!/home
Search or browse available datasets

## Slide 39: Atmosphere Data Store (ADS)
https://ads.atmosphere.copernicus.eu/cdsapp#!/home

## Slide 40: Atmosphere Data Store (ADS)
https://ads.atmosphere.copernicus.eu/cdsapp#!/home
Product overview gives data description and list of available variables

## Slide 41: Atmosphere Data Store (ADS)
https://ads.atmosphere.copernicus.eu/cdsapp#!/home
Choose variables, model, level, date, time, area for API request of download as netcdf file

## Slide 42: Further information and user support for CAMS
Further information: http://atmosphere.copernicus.eu/ | @CopernicusECMWF @ECMWF
User support: https://atmosphere.copernicus.eu/cams-user-service-desk/

## Slide 43: THE ATMOSPHERE MOOC
#AtmosphereMOOC
https://www.atmospheremooc.org/course-overview

## Slide 44
Go to:
https://ltpy.adamplatform.eu
1
2
Create an account: https://wekeo-login.services.meeo.it
Access to the practical course material via Jupyterhub
User Workshop and Training on Fire Monitoring