## Slide 1
UV-Vis remote sensing instruments - Retrieval and satellite validation
M. Van Roozendael (BIRA-IASB)

## Slide 2: Content
Passive UV-Vis DOAS instruments
Retrieval methods
Networks
Satellite validation (Sentinel-5p)
Conclusions and perspectives

## Slide 3: Passive UV-Vis remote-sensing
Space nadir geometry (e.g. Sentinel-5p)
DOAS spectral fitting
Slant column
Molecular absorption cross-sections
AMF calculation
Vertical column
Radiative transfer model
Ancillary informations on atmospheric and surface parameters

## Slide 4: Passive DOAS : the many possible geometries
Det
Det
Det
Det
Direct-sun
Balloon-borne
Airborne multi-axis
Zenith-sky
Multi-axis (MAXDOAS)
Imaging DOAS
Satellite nadir
Satellite limb
Satellite occultation

## Slide 5: Ground-based DOAS instruments
IUP-B
BIRA
Pandora
Phaeton
CU-Boulder
AIOFM
Airyx Skyspec
SAOZ
Telescope/lens
Entrance optics
Grating spectrometer
Fiber optic
Array detector
(CCD)

## Slide 6: Direct-sun (or direct moon)
Direct sun/moon signal:
= Signal outside atmosphere
after attenuation
(by scattering or absorption)
on the way to the instrument
 high accuracy for total column retrieval
Light path well defined

## Slide 7: Zenith scattered-light DOAS technique
Simple geometry, but the light path is more complex
Used for mobile measurements and to retrieve stratospheric trace gases at twilight
Det
SAOZ
Trace gas layer
z
Scattering height
Contains information on the vertical distribution of gases in the stratosphere (due to the progressive rise of the scattering height during twilight)
Using suitable inversion tools (OE), allows to retrieve vertical profiles in the stratosphere (NO2, BrO, O3)

## Slide 8: MAX-DOAS (Multi-AXis DOAS)
More complex geometry, but contains more information on the tropospheric composition
Measure sky-spectra at different telescope elevations
The length of the light path in the lower troposphere (close to the surface) is different for each elevation
Can be used to derive the vertical distribution of gases in the troposphere
When subtracting zenith measurements from off-axis ones, the stratospheric absorption can be eliminated

## Slide 9: MAX-DOAS (Multi-AXis DOAS)
Retrieval generally complex
For low elevations, the light-path depends strongly on multiple scattering effect due to air and particles
AMF calculations requires accurate multiple-scattering radiative transfer codes (e.g. LIDORT, SCIATRAN) and must account for aerosols
The information content is mostly contained in the lowermost troposphere (boundary-layer)
Best suited to retrieved short-lived tropospheric constituents (NO2, HCHO, glyoxal, SO2, HONO, BrO, IO …)
Typical clear-sky box-AMFs at 440 nm
Wittrock (2004)

## Slide 10: Aerosol retrieval using O2-O2 (O4) measurements
When present in the atmosphere, aerosols increase multiple-scattering and reduce the horizontal light path (so the O4 absorption)
Wagner (2004)
Clean troposphere (no aerosol)
Polluted troposphere
O4 absorption cross-sections
Because of its known concentration in air, O4 (O2 collisional complex) can be used to derive information on the light path length in the troposphere (and on aerosol content)

## Slide 11: MAX-DOAS retrieval using Optimal Estimation (OE)
Step 1: DOAS retrieval of slant columns (NO2 and O4)
Step 2: First optimal estimation (OE) step to retrieve aerosol profile from O4
Step 3: Second OE step to retrieve the trace gas profile (using the aerosol profile as an input)
Clémer et al., 2010

## Slide 12: Examples of MAX-DOAS retrievals
HCHO
NO2
 |  | Smoothing + noise error | Aerosol retrieval error | A-priori error | Absorption cross-sections | Total uncertainty
NO2 | VCD | 3 | 6 | 10 | 3 | 12
 | Surface conc. | 8 | 25 | 14 | 3 | 30
HCHO | VCD | 10 | 8 | 23 | 5 | 25
 | Surface conc. | 20 | 21 | 11 | 5 | 35
Typical error budget (polluted conditions)

## Slide 13: Global networks
NDACC UVVIS-WG
(Network for the Detection of Atmospheric Changes)
https://www.ndaccdemo.org/
SAOZ instrument
DOAS-ZSL and MAX-DOAS instruments (custom-made research systems or commercial)
Spectral range: 300 – 600 nm, 0.4-1.0 nm resolution FWHM
Approx. 30 stations worldwide in operation
Operational products: Total O3, stratospheric NO2 column
Scientific products
- Stratospheric BrO and OClO columns
- Tropospheric NO2, HCHO columns and profiles (DOFs ~ 2)
SAOZ data centrally processed at CNRS/LATMOS
MAX-DOAS central processing under development (FRM4DOAS)
PGN
(Pandonia Global Network)
https://www.pandonia-global-network.org/
Pandora instrument
Direct-sun/moon and sky measurements
Spectral range (S1): 300 – 550 nm, 0.7 nm resolution FWHM
> 50 stations worldwide in operation – fast growing network
Operational products: total O3 and NO2 columns
Other products:
- Total SO2 and HCHO columns
- Tropospheric NO2 columns and surface concentration
Central calibration of instruments
Central processing using operational Blick software

## Slide 14: NDACC and associated UV-VIS instruments
SAOZ

## Slide 15: PGN instruments distribution (20 October 2020)
Currently in process of giving certificates to make instruments “official” (from red to green in map)

## Slide 16: Other networks and emerging activities
JAMSTEC network over Japan and Asia https://ebcrpa.jamstec.go.jp/maxdoashp/
SKYNET (Chiba University) http://atmos3.cr.chiba-u.jp/skynet/pantnagar/pantnagar.html
BREDOM (Bremen University) http://www.iup.uni-bremen.de/doas/groundbased_data.htm
Various independent research groups
Aerosols, Clouds and Trace gases Research Infrastructure
‘Distributed’ European Research Infrastructure with research facilities around the world
22 European countries / > 100 RPO have committed to ACTRIS
NDACC, Pandonia and SAOZ components in CREGARS topical center
http://actris.net/

## Slide 17: Role of UV-Vis reference networks in Sentinel-5p mission

## Slide 18: End-to-end validation of S-5p NO2 product
Harmonised, end-to-end validation of TROPOMI NO2 retrieval: stratospheric, tropospheric and total NO2 vs. ZSL-DOAS, MAX-DOAS and PGN monitoring networks

## Slide 19: Operational monitoring of S-5p NO2 stability
Processor version switch (v1.2 -> v1.3)

## Slide 20: HCHO: scientific validation of S-5p and OMI products
TROPOMI
OMI
Courtesy I. De Smedt, BIRA

## Slide 21: Testing a novel approach to S5p SO2 retrieval using Pandora*
S5p operational
S5p COBRA
COBRA = Covariance-Based Retrieval Algorithm
-> new approach to S5p SO2 retrieval, alternative to DOAS
(Nicolas Theys, BIRA)
*non-operational Pandora data

## Slide 22: Validation of S5p innovation OClO product
Eureka (U. Toronto)
Ny Alesund (IUPB)
Eureka (U. Toronto)
Kiruna (MPIC)
Harestua (BIRA-IASB)
Arrival Height (IUPH)
Neumayer (IUPH)
Belgrano (INTA)
Marambio (INTA)
G. Pinardi (BIRA-IASB)
A. Richter (IUPB)
NDACC
S5p Innovation

## Slide 23: MetOp-A & B GOME-2 glyoxal products
MAM
GOME-2A
GOME-2B
S5p Innovation

## Slide 24: Issues and perspectives
Improve treatment of clouds and aerosols (reduce uncertainties)
Improve QA/QC methods
Network data consistency ( central processing, interoperability)
Better understand spatial representativeness of measurements
New retrieval developments
  Additional species (glyoxal, SO2, HONO, …)
  Improve vertical profile inversion algorithms (O3, NO2, ….)
  Develop advanced methods to retrieve information on small-scale horizontal structures (NO2). Can be obtained making use of multi-angular, multi-wavelength MAX-DOAS measurements and/or deployment of city-scale networks of instruments (tomography)
Optimise global network deployment

## Slide 25: Network deployment
S5p NO2
S5p HCHO
Some key emission regions are not covered enough by current networks

## Slide 26: Conclusion
Ground-based UV-VIS remote sensing is developing as an important contribution to Fiducial Reference Measurements (FRMs) for atmospheric composition
Implies activities around:
  Network development (PGN, NDACC, …)
  Calibration facilities and establishment of best practices
  Algorithms and product developments
  Central processing facilities
  Interoperability (common standards and data formats)
Supported by Space Agencies (ESA, NASA, KARI, …)
Integrated in ACTRIS research infrastructure
Key element of the geostationary satellite constellation of observing systems, started with OMPS, Sentinel-5p, EMI and GEMS (first AQ sensor on GEO)