## Slide 1
Satellite Applications on Aerosols:
From Local Sources to Long Range Transport
Anu-Maija Sundström, Finnish Meteorological Institute & EUMETSAT Atmospheric Composition Monitoring SAF (AC SAF)

## Slide 2
Contents of the Lecture
Introduction
Satellite Observations of Aerosols
  AOD
  Absorbing Aerosol Index
  Absorbing Aerosol Height
Example case: US Fires in September 2020

## Slide 3
Animation created by Antti Lipponen, FMI, based on NASA Global Modeling and Assimilation Office (GMAO) GEOS FP analysis.
AEROSOLS
Solid or liquid particles suspended in the Earth’s atmosphere.
Sizes vary from nanometers (1 nm =10-9 m) to hundreds of micrometers (1 μm = 10-6 m).
Either emitted directly into the atmosphere (primary aerosols) or formed via gas to particle conversion (secondary aerosols).
Sources are both anthropogenic and natural.
Residence time in the atmosphere typically from few days to weeks.

## Slide 4: Optical Remote Sensing Measurements of Aerosols
Ground-based
Satellites
Active
Lidars, Ceilometers
Aerosol vertical profiles
Passive
Sunphotometers
Optical depth & various other retrieved parameters
Active
Space-based lidars
Aerosol vertical profiles
Key aerosol properties:
Aerosol loading ->optical thickness (”how much?”)
Aerosol size distribution, size vs. radiation wavelength
Aerosol chemical composition (type)
  Complex refractive index; single scattering albedo
Limited number of general aerosol type categories that have distinctly different optical properties
Passive
Spectroradiometers
Optical depth, absorbing aerosol Index
Various other parameters e.g. layer height, fine mode fraction etc.

## Slide 5
Aerosol Optical Depth (AOD)

## Slide 6
Aerosol optical depth (AOD)
Also known as aerosol optical thickness (AOT)
AOD is related to the amount of (optically active) aerosols in the total atmospheric column.
Retrieved from satellite- and ground-based instruments
Extinction coefficient:
units of inverse length [m-1]
AOD is defined as the sum of aerosol extinction at all atmospheric levels, from surface up to the top of the atmosphere
[unitless]
Measured aerosol size distribution
Contribution of each particle size to the total extinction at 550 nm

## Slide 7: AOD retrievals
Reflectance at TOA measured by satellite
Atmospheric path reflectance:
aerosols
molecules
Surface contribution
TOA reflectance measured by the satellite
Cloudscreening
Surface correction
Rayleigh correction
Aerosol contribution
”Dark” Surface
”Bright” Surface
From Tian & Sun, 2016
Bright surface
Dark surface
No aerosols
Aerosol overlay

## Slide 8
AOD is wavelength dependent
  often given at 550 nm.
AOD doesn’t tell about vertical distribution of aerosols.
  However, often aerosols are located within the lowest few kilometers.
Satellite AOD is available from several instruments (and wavelengths), e.g.:
  OLCI, SLSTR (Sentinel 3), AATSR (Envisat, until 2012)
  MODIS (Aqua, Terra), MISR (Terra), SeaWIFS…
  Multi-instrument products such as PMAp (combining information from GOME-2, AVHRR, IASI)

## Slide 9: MODIS Terra AOD (at 550 nm) 2019
Global mean AOD at 550 nm: about 0.15
Typical range of variation at 550 nm: 0.05…2.0
AOD timeseries of > 20 years are available (e.g. Sogacheva et al. 2020 )
Dust
Biomass burning
Biomass burning
Biomass burning
Anthropogenic pollution
Dust
Biomass burning

## Slide 10: (Satellite) AOD vs. (in situ) Particulate Matter (PM)
Global and national air quality standards considering aerosols are based on the amount of particulate matter (PM, [μg/m3])
  PM10: inhalable particles, with diameters 10 μm and smaller
  PM2.5: fine inhalable particles, with diameters 2.5 μm and smaller
AOD and PMs are both related to aerosol concentration.
Satellite-based AOD has been used in many applications to estimate e.g. global PM2.5 concentrations (see e.g. Van Donkelaar et al., 2010, 2016)
AOD
total column -> elevated layers possible.
can’t distinguish aerosols exactly by their physical size
At ambient relative humidity
PM
Surface concentration
Measurement of specific sizes, also aerosols that are too small for satellites ”to see”.
Defined from dry particles

## Slide 11
Absorbing Aerosol Index (AAI)

## Slide 12: Absorbing Aerosol Index (AAI)
  Also known as UV Aerosol Index (UVAI)
  Defined using UV-wavelengths (typically 340 – 380 nm; GOME-2, TROPOMI, OMI, OMPS)
  Sensitive to absorbing aerosols: smoke, volcanic ash, desert dust
  AAI separates the spectral contrast at two UV wavelengths caused by aerosol extinction from that of other effects (e.g. molec. scattering)
  Can be obtained also for cloudy scenes, where aerosols are on top of clouds.
AAI is a good tracer for smoke and dust/ash plumes

## Slide 13
Positive AAI values indicate presence of absorbing aerosols
  For clouds (or scattering aerosols) AAI is close to zero or negative
  Also sunglint over ocean causes positive values but that is often filtered out from the data.
For plumes typically AAI > 1.0
  Background typically slightly positive
Interpreting AAI (1)
Sun glint
Smoke plume from Canadian forest fires
Desert dust
AAI is available from several instruments:
GOME-2 (A,B,C)
TROPOMI
OMI, OMPS
Multi-instrument AAI (> 40 year time series! )

## Slide 14
AAI values depend on various factors
  Comparing cases is not straightforward!
Not a ”direct” measure of aerosol loading
With AAI you typically see an elevated plume
  For assessing air quality at the surface, additional information (model, in situ) is recommended.
Interpreting AAI (2)
From: Ginoux & Torres, JGR, 2003
”Increasing aerosol loading”
Abs. aerosols at 6 km height
Abs. aerosols at 2.5km height
Abs. aerosols at 1.5km height
(single scatt. albedo)

## Slide 15: AOD vs. AAI: India and China, 4.11.2019
AOD at 550 nm
On 4.11. in India and China AOD (550 nm) was very high (0.5…2.0)
The same day AAI was elevated only in India.
AAI
Why the difference?
Aerosol type!
AOD -> all optically active aerosols, related to aerosol amount.
AAI -> only absorbing aerosols! Depends on the amount but also on many other factors

## Slide 16
Absorbing Aerosol Height (AAH)

## Slide 17: GOME-2 Absobing Aerosol Height
Retrieval is based on Oxygen A-band and information derived from FRESCO cloud algorithm.
AAH is provided from GOME-2 (A,B,C) and can be obtained via AC SAF FMI server.
AAH should be analysed with AAI:
  AAI < 2 correspond to scenes with too low amounts of aerosol to result in a reliable AAH -> pixels have fill value.
  2 < AAI < 4: aerosol layer is not in all cases thick enough for a reliable retrieval, but AAH estimate is given, should be used with caution.
AAH also available from TROPOMI
Example of GOME-2 (A,B,C) AAH

## Slide 18: Fires in the US: September 2020
PMAP AOD
GOME-2 (A,B,C) Absorbing Aerosol Index
GOME-2 (A,B,C) Absorbing Aerosol Height

## Slide 19
Detected fires over the US in September 2020
MODIS Coll. 6 FRP
In early September largest fires and smoke were concentrated in the West coast
GOME-2 AAI

## Slide 20
GOME-2 AAI
GOME-2 AAH
As more fires were ignited, also meteorological conditions changed and significant aerosol transport towards Europe was observed.
PMAP AOD at 550 nm

## Slide 22
Take Home Messages
Satellites offer an efficient way to monitor aerosols on a global scale.
AOD, AAI and ALH can be used in many applications: from analyzing local aerosol sources to long-range transport.
  It is important to remember the interpretation of each parameter.
For air quality assesment, it is recommended to combine information from several sources; e.g. satellite data and models
References:
Tian and Sun: Retrieval of Aerosol Optical Depth over Arid Areas from MODIS Data, Atmosphere, 7(10), 134 2016.
Sogacheva et al.: Merging regional and global aerosol optical depth records from major available satellite products, Atmos.Chem. Phys, 20, 2020
Ginoux & Torres: Empirical TOMS index for dust aerosol: Applications to model validation and source characterization, JGR, 108, 2003.
Van Donkelaar et al.: Global estimates of ambient fine particulate matter concentrations from satellite-based aerosol optical depth: development and application, Environ. Health. Perspec. 118, 2010.
Van Donkelaar et al.: Global Estimates of Fine Particulate Matter using a Combined Geophysical-Statistical Method with Information from Satellites, Models, and Monitors, Environ.Sci. Technolog., 50, 2016.