## Slide 1
MTG Mission overview
Natasa Strelec Mahovic
EUMETSAT
Summer School 2025

## Slide 2: Current EUMETSAT satellites (10)
Meteosat Second Generation
Two-satellite system
Full disc imagery mission (15 mins) (Meteosat-11 (0°))
Rapid scan service over Europe (5 mins) (Meteosat-10 (9.5° E))
METEOSAT-9 (45.5° E)
METEOSAT-10, -11
SENTINEL-3A & -3B (98.7° incl.)
Copernicus satellites delivering marine data services from 814km altitude
Low Earth, sun-synchronous orbit
JASON-3 (63° incl.)
Low Earth, non-synchronous orbit
Copernicus ocean surface topography mission (shared with CNES, NOAA, NASA and Copernicus)
Metop-B
Metop-C
Sentinel-3A
Geostationary orbit
Geostationary orbit
Meteosat Second Generation providing Indian Ocean data coverage
Sentinel-3B
Jason-3
Meteosat-10
Meteosat-9
Meteosat-11
METOP-B & -C (98.7° incl.)
Low Earth, sun-synchronous orbit
EUMETSAT Polar System (EPS)/ Initial Joint Polar System
Sentinel-6
Michael Freilich
Sentinel-6 Michael Freilich (66° incl.)
Low Earth, non-synchronous orbit
Copernicus ocean surface topography mission (shared with NASA, NOAA, ESA and Copernicus with support from CNES)
Meteosat-12 (MTG-I1)
METEOSAT-12 (MTG-I1)
Geostationary orbit
Meteosat Third Generation
Full disc imaging mission (10 min)
Notes: The current status of EUMETSAT satellite fleet. EUMETSAT operates 10 satellites, 4 geostationary and 6 polar orbiting. We will be focusing on geostationary today and in particular the new Meteosat 12 satellite or MTG-I1 as it was called.

## Slide 3: Current EUMETSAT geostationary satellites
METEOSAT-9
45.6-45.9° E
Indian Ocean data coverage (IODC)
Delivers the EUMETSAT best-effort contribution to the multi-partner IODC services.
METEOSAT-11
9.5° E
Rapid Scan Service (RSS)
Delivers the Meteosat secondary RSS service over Europe and adjacent seas.
METEOSAT-10
0° longitude
Full Earth Scan imagery
Provides the Meteosat primary full-disc imagery service over the European continent, Africa and parts of the Atlantic and Indian oceans.
METEOSAT-12 (MTG-I1)
0.3° W
Full Earth Scan
Lightning imager
MTG-I1 was successfully launched on 31 December 2022
Operational since 4 December 2024
Notes: Correct orbits in image

## Slide 4: EUMETSAT next generation satellites
MTG-I1 (Meteosat-12)
Launched: 13 Dec 2022 Operational: 4 Dec 2024
Status: July 2025
Launch: August 2025
2026
Launched on 1 July 2025
2026

## Slide 5
MTG Mission

## Slide 6: MTG-I imaging mission
Imagery mission implemented by two MTG-I satellites:
  Full disc imagery every 10 minutes in 16 bands
  Fast imagery of Europe every 2.5 minutes with MTG-I2 (’26/’27)
New Lightning Imager (LI)
Operational exploitation: ~2024-2044

## Slide 7: MTG-S sounding mission (launched on 1 July 2025)
Hyperspectral infrared sounding mission
3D weather cube: temperature, water vapour, O3, every 30 minutes over Europe
Air quality monitoring and atmospheric chemistry in synergy with Copernicus Sentinel-4 instrument
Operational exploitation: ~2025-2045

## Slide 8: MTG system overview
MTG-I
16 spectral channels over Europe every 2.5 minutes
Rapid Scanning Service
MTG-S
Hyperspectral Infrared Sounder
Copernicus Sentinel-4 UVN
Full Disc sounding service
MTG-I
16 spectral channels over Europe and Africa every 10 minutes
Full Disc image service
EUMETSAT Central Facilities
Mission Control Centre
Product processing
Data archive
Data dissemination
Darmstadt, Germany
Telemetry, telecommand and control
Ground stations
Fucino, Italy and Cheia, Romania
Mission data acquisition
Ground stations
Leuk, Switzerland and Lario, Italy
EUMETSAT SAF Network
Satellite Application Facilities
Product processing
EUMETSAT member states

## Slide 9: MTG Mission Objectives
MTG-I
16 spectral channels over Europe every 2.5 minutes
Rapid Scanning Service
MTG-S
Hyperspectral Infrared Sounder
Copernicus Sentinel-4 UVN
Full Disc sounding service
MTG-I
16 spectral channels over Europe and Africa every 10 minutes
Lightning Imager
Full Disc image service
Primary mission:
Support Nowcasting/ Short Range Forecasting of high impact weather
  This is achieved through:
  Continuity and enhancement of MSG imagery
  Addition of a new lightning imaging capability
  New, innovative infrared hyper-spectral sounding
Secondary mission:
Air quality monitoring over Europe
  This is achieved through:
  Synergy between Sentinel-4, Infrared Sounder and Imagery

## Slide 10
MTG–I
Flexible Combined Imager (FCI)

## Slide 11: Performance Enhancements of Spectral Imager
SEVIRI on current Meteosat Second Generation satellites | FCI on new Meteosat Third Generation satellites
15 min full disc repeat cycle | 10 min full disc repeat cycle
SNR 1.2 to 10.1 | SNR 12 to 40
NEdT 0.25-1.8K | NEdT 0.1-0.3K
IR3.9 up to 335K | IR3.8 up to 450K
11 x 3.0 km non-HRV channels | Normal resolution (FDHSI): 8 x 1.0 km channels 8 x 2.0 km channels
1.0 km High-Res Visible channel | High resolution (HRFI): 2 x 0.5 km channels 2 x 1 km channels
 | New channels VIS0.4 VIS0.5 VIS0.9 NIR1.3 NIR2.2
SEVIRI
FCI
SNR - Signal-to-Noise Ratio: indicates the strength of the desired signal relative to the background noise. A higher SNR - clearer signal with less interference, lower SNR -weaker signal overwhelmed by noise.
NEdT- Noise Equivalent Differential Temperature:
A measure of a sensor's radiometric sensitivity, indicating the smallest temperature difference that the sensor can reliably detect.

## Slide 12: MTG-I Flexible Combined Imager (FCI) - Scanning Services
To support the Full Disc Scanning Service, the FCI on MTG-I1 will sample all channels of the Full Disc every 10 minutes.
Operational
To support the Rapid Scanning Service, FCI on MTG-I2 will sample all channels in the top quarter of the Full Disc every 2.5 minutes.
Expected launch in 2026

## Slide 13: Spatial resolution – SEVIRI 3km

## Slide 14: Spatial resolution – FCI 500m

## Slide 15
SEVIRI Natural Color 3km
18.03.2023 11:45 UTC
FCI True Color 1km
18.03.2023 11:50 UTC
FCI 0.6µm 0.5km
18.03.2023 11:50 UTC
SEVIRI 0.6µm 3km
18.03.2023 11:45 UTC

## Slide 16: Spatial resolution
SEVIRI VIS0.6 SEVIRI HRV FCI VIS0.6
3 km 1 km 500 m

## Slide 17: MSG SEVIRI– channels
3=VIS0.6
4=VIS0.8
7=NIR1.6
9=IR3.9
10=WV6.2
11=WV7.3
12=IR8.7
13=IR9.7
14=IR10.8
15=IR12.3
16=IR13.3
Solar channels
available with
3 km resolution
Thermal channels
available with
3 km resolution
HRVIS
HRVIS channel
available with
1 km resolution

## Slide 18: MTG FCI – channels
3=VIS0.6
4=VIS0.8
7=NIR1.6
9=IR3.8
10=WV6.2
11=WV7.3
12=IR8.7
13=IR9.7
14=IR10.5
15=IR12.3
16=IR13.3
1=VIS0.4
2=VIS0.5
5=NIR0.9
6=NIR1.3
8=NIR2.2
Solar channels
available with
1.0 km (& 0.5 km)
resolution
Thermal channels
available with
2 km (& 1 km)
resolution

## Slide 19: MTG FCI – channels
5 VIS
3 NIR
8 IR

## Slide 20: MTG FCI new RGBs

## Slide 21: True colour RGB

## Slide 22: Cloud Phase RGB
Small ice particles
Small droplets,
thick clouds
Large droplets, thick clouds
Large ice particles
Enables separation of water from ice clouds and offers information on cloud top particle size
The Cloud Phase RGB is useful for convection monitoring
Limited to daytime applications

## Slide 23: Snow vs. low clouds

## Slide 24: Cloud Type RGB
Best RGB to see thin cirrus clouds
Clear distinction of low level water clouds

## Slide 25: New WV absorption channel 0.9 μm
  Channels:
  0.9 μm
  6.7 μm
  7.3 μm
  Humidity profile, total column precipitable water
  Applications:
  NWP
  Nowcasting
humidity area
- based on 0.9 μm channel
Moisture fields describing the pre-convective environment
new FCI channel 0.9 µm /0.8 µm

## Slide 26: Fire Temperature RGB
Smoke
Fire core
Burn Scar

## Slide 27
MTG–I
Lightning Imager (LI)

## Slide 28: MTG Lightning Imager
Lightning is a sudden electrostatic discharge between electrically charged regions:
  of a cloud (intra-cloud lightning or IC)
  of two clouds (cloud-to-cloud lightning or CC)
  of a cloud and the ground (cloud-to-ground lightning or CG)
Total lightning
= cloud-to-ground + intra-cloud lightning
Lightning is a precursor of severe weather, with a lead time of tens of minutes
The radiation produced by an electric discharge within or below a cloud reaches the cloud top after multiple scattering through the cloud and is detected by lightning imagers in space
MTG LI measures total lightning
Foto: Daniel Pavlinovic
A flash from space

## Slide 29: MTG Lightning Imager
LI in a nutshell | 
Spatial Resolution at Nadir | 4.5 km (variable throughout the Filed of View, FOV)
Spectral band | 777.4 nm and 1.9 nm narrow band
Detector(s) | 1000 x 1170 pixel (x 4) CMOS
Frame rate | 1 ms (1 kHz acquisition frequency)
On-board processing | Background evaluation and subtraction Lightning detection On-board filtering
Bandwidth | 30 Mbps
Manufacturer | Leonardo (Italy) under the industrial prime contractor Thales Alenia Space (France)

## Slide 30: MTG Lightning Imager (LI)

## Slide 31: MTG Lightning Imager (LI)

## Slide 32: LI vs ground-based Lightning Location Systems (LLSs)
SPACE-BORNE
An optical detector that registers lightning optical emissions at the cloud tops, e.g., LI, GLM.
GROUND-BASED
A network of radio sensors plus central station that compares the observations of the sensors and computes lightning locations, e.g., NORDLIS, EUCLID, GLD360.
1. Cloud-top emission
2. LI observation every 1 ms
3. LI Lightning Events (LEs)
Notes: You are probably familiar with using NORDLIS, EUCLID, maybe also GLD360. All these detect radio emissions by lighting while the LI detects optical emission from space at 777.4 nm.
Explain briefly how optical emission as seen from space is converted into LI LEs (bottom 3 images).

## Slide 33: LI raw data: Lightning Events (LEs) + Background Images (BCK)
1-minute real-speed animation of LI raw data in central Africa.
Green pixels on top of the BCK image represent cloud-top illuminations that triggered LI LEs.

## Slide 34: LI raw data: Lightning Events (LEs) + Background Images (BCK)
Notes: This is a public outreach video from May 2024. Can see how cold-frond thunderstorms form and develop in the south of Germany on 2 May 2024.

## Slide 35: MTG Lightning Imaging mission

## Slide 36: MTG Lightning Imaging mission

## Slide 37: Level 2 Group Product – LI-L2-LGR
LI pixel |  |  |  | 
LI Group
Collection of connected (pixel side touching) DTs on a single acquisition frame.
Group location is the radiance weighted centroid of its LE (lightning events) locations.
LGR can be made of 1 or more LEs (the example on the left is a 4 LE group).
LI groups represent ground lightning strokes and cloud lightning pulses in ground-based LLS data.
  However, a pulse/stroke often triggers a sequence of many LI groups as the optical emission often lasts longer than 1 ms LI integration frame.
Lightning Group of 12 LEs
Single-event Lightning Groups
Lightning Group of 9 LEs

## Slide 38: Level 2 Flash Product – LI-L2-LFL
LI Flash
Collection of Groups that are correlated in space (16.5 km) and time (330 ms).
Flash location is the radiance-weighted centroid of its group locations.
LFL can be made of 1 or more LGRs.
LI flashes roughly correspond to flashes in ground-based LLS data.
  This applies more to general flash statistics (storm level and above).
INDIVIDUAL GROUPS (10x SLOWDOWN)
BUILDING UP ~2-SECOND FLASH (10x SLOWDOWN)
An example of a L2-LFL (right) being built up from individual L2-LGRs, made of individual LEs in a continuous sequence of 1 ms LI integration frames (left).
Note that this example is a very large and long-lasting ‘megaflash’ in Africa.

## Slide 39: LI-L2-LGR vs ground-based lightning strokes/pulses
N = 120 652
N = 9 582
Similar spatial storm pattern between LI LGR clusters and ground-based GLD360 stroke/pulse clusters.
Note the ~12x greater number of LI LGRs, compared to GLD360 strokes/pulses.

## Slide 40: LI L2 data demo – Comparison with surface-based lightning detection data
LI and the three ground-based LLSs all observed very similar space-time patters of lighting, storm development and movement.
storms in southern Germany 02 May 2024

## Slide 41: LI L2 data demo – LI flashes on 6 May 2024
LI Flash locations during 24 hours on 2024-05-06, colored by hour.
The polygons represent the field-of-view of individual LI cameras.
A total of ~1.3 million flashes, made of 19.8 million groups (i.e., an average of ~15 groups per flash).
Note also the presence of some False Alarms (isolated flashes in space and time.

## Slide 42: LI L2 data demo – 24H of lightning flashes around Italy

## Slide 43: LI L2 data demo – a week of lightning flashes in Europe

## Slide 44: Level 2 gridded products – LI-L2-AF (Accumulated Flash)
LI Pixel |  |  |  | 
 | 1/10 | 1/10 | 1/10 | 
 |  | 1/10 | 2/10 | 
 |  |  | 1/10 | 
 |  | 1/10 | 1/10 | 1/10
frame n
frame n + 1
frame n + 2
  LI Level 2 Accumulated Flash (AF)
  Allows one to keep track of the density of events within the flash and within sequences of accumulated flashes
Accumulation over 3 frames

## Slide 45: Level 2 gridded products – LI-L2-AFA (Accumulated Flash Area)
LI Pixel |  |  |  | 
 | 1 | 1 | 1 | 
 |  | 1 | 1 | 
 |  |  | 1 | 
 |  | 1 | 1 | 1
  LI Level 2 Accumulated Flash Area (AFA)
  Allows one to keep track of the areas touched by multiple flashes (does not provide the event density)
frame n
frame n + 1
frame n + 2
Accumulation over 3 frames

## Slide 46: Level 2 gridded products – LI-L2-AFA (Acc. Flash Radiance)
LI Pixel |  |  |  | 
 | R1 | R2 | R3 | 
 |  | R4 | R5+R5’ | 
 |  |  | R6 | 
 |  | R7 | R8 | R9
  LI Level 2 Accumulated Flash Radiance (AFR)
  Allows one to represent the total radiance within a certain pixel from multiple flashes
frame n
frame n + 1
frame n + 2
Accumulation over 3 frames

## Slide 47: Level 2 gridded products
It’s up to you to find out which one is best (in a particular weather/storm situation).

## Slide 48: Potential of LI data for nowcasting
Significant potential of LI data for nowcasting of severe convective storms.
Sizes of red dots relative to LI flash size.

## Slide 49: 12 July 2024: Thunderstorms over CH/I/D
Lightning “jump”
Lightning “jump”
Lightning “jump”
Lightning “jump”

## Slide 50: 12 July 2024: Thunderstorms over CH/I/D
“Lightning hole”:
1. Core of storm too optically dense for lightning signal to penetrate
2. Lack of lightning activity due to updraft being too strong for generation of charged particles

## Slide 51: 7 Aug 2024: Multicells and Bow Echo over N Italy

## Slide 52: Some preliminary findings on LI in Europe/high latitudes
LI performs good and detects a lot of lightning in Europe and even at high latitudes (i.e. around 60 degrees north).
In many cases, LI detects more lightning than ground-based systems in Europe.
  there is a need for more comparisons against short-range systems such as EUCLID and NORDLIS.
There are also storms where LI clearly detects less than ground-based lightning location systems.
  E.g. some storm cells in widespread and strong convective systems in central Europe in July 2023 showed some LI detections but significantly more ground-based detections.
  LI is affected by cloud optical thickness – very tall and thick thunderstorms can hide lightning from the LI (needs more investigation).
  The cloud optical thickness should theoretically be less of a concern in smaller (developing) thunderstorms, also around the time the first flashes appear (needs more evidence).
Keep in mind the presence of some False Alarms – best to cross-check LI isolated flashes against developing radar/satellite cloud signatures.
(These preliminary conclusions are based only on a limited number of storms in summer 2023 and spring 2024)

## Slide 53
MTG–S
Infrared Sounder (IRS)

## Slide 54: MTG Infrared Sounding mission
https://youtu.be/kuLkXq2VKXE?t=26

## Slide 55: MTG Infrared Sounding mission
LAC4
LAC3
LAC2
LAC1
time
Spectrum
Interferogram
L1
wavenumber
L0
Single spatial sample
The Earth disk is split in 4 Local Area Coverage (LAC) zones, each of them covered in 15 min by a succession of “steps and stares” called dwells
LAC4 (northern mid-latitudes) will be covered every 30 minutes
LAC1, 2, 3 will be alternatively viewed in-between

## Slide 56: MTG Infrared Sounding mission
Operational spectro-imagery at high spectral, spatial & temporal resolution:
Two spectral bands: MWIR: 1600 to 2250 cm-1 (4.44–6.25 µm) and LWIR: 680 to 1210 cm-1 (8.26–14.70 µm)
Sampling: 0.6cm-1 spectral, 4km at nadir spatial, 30min temporal over Europe and parts of North Africa
Expected weighting functions of IRS spectral channels

## Slide 57
Convective Storm case 24 June 2021
IRS Test data
IRS L2 State Vector Product:
  Profiles (temperature, humidity, ozone)
  Surface parameters
  Instability indices and total vertical column
  Cloud products
6 hours (08:15-14:00 UTC) of simulated MTG-IRS geophysical products (Level 2) at 30-min intervals over Local Area Coverage 4 (LAC4)
Based on ECMWF IFS 9-km model analyses and grid, and CAMS 54-km model reanalyses
24 June 2021: Major convection case in Poland, Czech Republic (F4 tornado)
Source: Catastrophic tornado in the Czech Republic | EUMETSAT - User Portal
SIMULATED MTG InfraRed Sounder Dataset for Nowcasting:

## Slide 58
Thank you!
Questions are welcome.